IoT Assignment – Packet Analysis 2
Report

The provided capture contains packets that are based on the IEEE 802.15.4 ZigBee protocol stack. The analysis of the packet capture is split into two sections:

1. Statistics
2. Technical Analysis
3. Decryption Attempts

Statistics
- There are 139 packets transmitted in total, which amounted to a size of 5180 bytes.
- The packet size limit is 128 bytes.
- The total capture time i.e. the time taken between the first and the last packet is exactly 77.411 seconds.
- The speed of transmission amounted to 1.796 packets per second on an average.
- In bytes, this is equal to 66.915 bytes per second.
- Each packet is sized at an average of 37 bytes.

The rate of packet transmission is better explained in the graph given below:

Technical Analysis
- There are two devices whose communication is captured in the packet capture. Their addresses are 0xa8a1 and 0x0000.
- The communication between the above devices have made it clear that there is only one network, and the PAN ID of the network is 0x595e.
- There are certain messages sent with destination address as 0xffff, these imply that those messages are broadcast messages.
- The coordinator in the network appears to be device with the address 0x0000.
- We can see that the data that is being sent over the network is through the ZigBee Network Layer, and we can see that there is bi-directional communication between the nodes with address 0x0000 and 0xa8a1.
- This data is divided into two; data that is tranferred from the device with address 0xa8a1 to the device with address 0x0000, and the data that is transferred from the device with address 0x0000 to the device with address 0xa8a1.
- Both flows of data are in hexadecimal format; and packets of each flow have consistent length, which leads to the conclusion that the data is encrypted.
- Moreover, this suspicion is confirmed by inspecting the ZigBee security header and the frame control field of the ZigBee network layer, which indicate the flags corresponding to security mechanisms i.e. encryption set to true.
- Upon further research, we understand that the ZigBee devices send data with the AES encryption standard, specifically the AES 128-bit CCM (Counter with CBC) standard, which provides both confidentiality and message integrity.
- There are multiple ways to decrypt the data, if the key is known. However the key is not known, and we resort to running attacks on the ciphertext.
- The ciphertext of both the flows are shown below:e

  Packet flow from 0x0000 to 0xa8a1:

Sl. No.	Packet Number	Data (Ciphertext)
1.	3	85df62dab35b3cc2
2.	8	67470977a0191b59
3.	12	8605845d31534c324
4.	16	72087d423b5bdc1d
5.	21	7e67c75cc094aa31
6.	25	e2e4cccd4b9c2311
7.	33	402b7f626ace30e7
8.	37	4acf99c0fcfe1bbe
9.	41	7ffa6f9dcce83c74
10.	45	d1a9f1442adbc499
11.	49	32bf659a085ee062
12.	54	0a786315756fb2fe
13.	58	8ecf4273dc6d4624
14.	62	ba4d76559532f2d9
15.	66	3daa30e8d3a19820
16.	70	64d6902c60d11b25
17.	74	57b44a46ff5dba26
18.	80	ea54f36f8a9bd52d
19.	84	9b37b4a5f68f7333
20.	88	cd01abe18e1eb8e8
21.	91	638c872ee6980eeb
22.	95	9dd03db54e40f7cc
23.	99	8fd35126cb6a768e
24.	116	5f195a000c9aeeee
25.	119	597df545c5c8188c
26.	123	14d7d264db7a0378
27.	127	e5d8994be9f474dd
28.	131	ac30e573b9beddcc
29.	136	cf23b3af1a7d5a65
30.	139	163264c2a2d508ba

  Packet flow from 0xa8a1 to 0x0000 (excl. bad packets):

Sl. No.	Packet Number	Data (Ciphertext)
1.	1	224ff22a813943b1e8658478a7d3d5
2.	6	7f77802534ba495d77023ed3a7aabd
3.	10	5e9d54052f901a58a4b510770e86f4
4.	14	f3f5b9f61984eaf3372d4fd93f2c0c
5.	19	c3779966a8e5c0603ccdaef234a56b
6.	23	ff4a25ffb703050c2d4e6e2ac0a95b
7.	31	eae6689b76035da42bfe346ee2c754
8.	35	4a76d7c531a80bd65b3cb0d10599d8
9.	39	9addf37076b4b6274b8316e7923fc3
10.	43	16704c1d71d523d015b7e8c50f1fd4
11.	47	e711f7892d92a26e0f7b4e22643418
12.	52	ce8bec700dd0158430b38caa710d0a
13.	56	b5a650ae3d2c84f0ed3ce0272bca58
14.	60	cc08d2a7164fc25af634bcd50dd70b
15.	64	283aac7bfeeaafb0db31da18e3a0be
16.	68	6e2780a0c9093506113d2a6ca66fda
17.	72	12e00c8ff4071045ef64aff5dddf7d
18.	78	00707d07ebc355d0c4299f8291c9a6
19.	82	a2d03dfc98b797471699ee5ee514c4
20.	86	d5c0335f74bb1c9d05953bb4369d54
21.	93	d143ae5c96b9375d4d95f20f7dfe88
22.	97	bd9f3fa376b1421517effe31dca2b4
23.	114	54de72035f2a6b56eb483eb02fe630
24.	117	f336750f914a29c82bef9decbb2927
25.	121	71931c305fba797fdb7f035ab202f6
26.	125	1c5113f2607f321639a4135a32f972
27.	129	94c111d4f1ffa1674d72ead3357917
28.	134	1075f389fee9c5762320ca1c6f4264

- An attempt was done to decrypt the data with the default Trust Center Link Key i.e. ZigbeeAlliance09 (5A:69:67:42:65:65:41:6C:6C:69:61:6E:63:65:30:39) but the attempt failed; thus proving that the devices do not use that key for encryption.
- Further analysis of the security fields of the packets show that the key used to encrypt the data is the Network key.
- Multiple decryption attempts were run with possible default network keys, but also did not succeed.
- The attempts are described in the third section.

Decryption Attempts
- The packet capture did not include the packet wherein the network key is sent from the coordinator to the other devices, so the key cannot be extracted out of the packet capture.
- The default Trust Center key i.e. ZigbeeAlliance09 (5A:69:67:42:65:65:41:6C:6C:69:61:6E:63:65:30:39) was loaded into Wireshark to automatically decrypt the packet capture, but it did not provide a successful result.
- The encrypted ciphertext was extracted and another attempt was done with a standalone decrypter which utilized the default Trust Center link key, but that did not work as well.
- A password list of probable passwords was generated and a bruteforce attack was run against the encrypted data, but it did not yield any positive results.
- The Killerbee security suite was also used with binary level dumps of firmware of ZigBee boards which were suspected to be the devices that were the transmitter devices, and side channel attacks were run with the said dumps, but no possible keys were found, and thus did not provide a successful result.